## Slide 1: Efficient Standard Co-Emulation Modeling Interface (SCE-MI) Usage to Accelerate TBA Performance
Ponnambalam Lakshmanan
Analog Devices, Bengaluru, India

## Slide 2: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 3: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 4: Acceleration Concept
Hardware assisted acceleration offers better performance over software simulation.
Hardware assisted acceleration techniques:
  Signal Based Acceleration (SBA)
  Transaction Based Acceleration (TBA)
  Embedded testbench
  Vector Based Acceleration (VBA)
  In-circuit Emulation (ICE)

## Slide 5: Transaction Based Acceleration
Traditional testbench is split into two domains
  Non-Synthesizable domain
    Runs on simulator
  Synthesizable domain
    Runs on emulator
Workstation
Emulator
Synthesizable
Non - Synthesizable

## Slide 6: Factors Affecting Acceleration
Various factors directly affect the emulator performance
  Inefficient usage of SCE-MI
  Behavioral constructs (Not purely-synthesizable)
  Memory Handling
  Amount of code running on simulator and emulator
  Simulator – Emulator synchronizations

## Slide 7: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 8: Introduction to SCE-MI
Standard Co-Emulation Modeling Interface (SCE-MI) is an Accellera standard
Communication interface between BFM and proxy
Different types of SCE-MI use models:
  SCE-MI Pipe based interface
  SCE-MI Direct memory interface (DMI)
  SCE-MI Function based interface

## Slide 9: SCE-MI Pipes
Salient Features:
  Unidirectional
  Batching
  Buffering
  Flushing
  Data shaping
  Blocking and Non-Blocking constructs

## Slide 10: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 11: Initial Architecture Challenges
Input SCEMI Pipes
Output SCEMI Pipes
Multiple SCEMI pipes
Transmission of small packets frequently
Async loop to clear pipe contents
Bottlenecks

## Slide 12: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 13: Optimizing SCE-MI Pipe Usage
Merging SCE-MI pipes
Challenge | Solution
Behavioral evals with every SCE-MI access | Send data via a single SCE-MI pipe. Static SCE-MI pipe - Bit vectors Dynamic SCE-MI pipe - Array of data

## Slide 14: Optimizing SCE-MI Pipe Usage
Synchronous access
Challenge | Solution
Asynchronous mode creates significant behavioral evals | Synchronous mode of SCE-MI pipe IS_CLOCKED_INTF = 1
scemi_input_pipe #(
.BYTES_PER_ELEMENT(20), .PAYLOAD_MAX_ELEMENTS(1),
.VISIBILITY_MODE(2),
.IS_CLOCKED_INTF(1) ) inbox (clk);
Code Snippet
s
scemi_input_pipe #(
.BYTES_PER_ELEMENT(20), .PAYLOAD_MAX_ELEMENTS(1),
.VISIBILITY_MODE(2),
.IS_CLOCKED_INTF(0) ) inbox (clk);
Code Snippet
s

## Slide 15: Optimizing SCE-MI Pipe Usage
Optimized data transfer
Challenge | Solution
Accessing more than one element per access results in behavioral evals PAYLOAD_MAX_ELEMENTS = 5; BYTES_PER_ELEMENT = 1; | If the intention is to access 5 Bytes per call then set PAYLOAD_MAX_ELEMENTS = 1; BYTES_PER_ELEMENT = 5;

## Slide 16: Optimizing SCE-MI Pipe Usage
Minimal Synchronization
Challenge | Solution
Frequent data transfer causes the emulator to halt frequently Results in degraded acceleration | Accumulate multiple bytes of data and transfer at once Try to buffer the elements Avoid unnecessary flush() usage
scemi_input_pipe #(
.BYTES_PER_ELEMENT(20), .PAYLOAD_MAX_ELEMENTS(1), .BUFFER_MAX_ELEMENTS(10),
.VISIBILITY_MODE(2),
.IS_CLOCKED_INTF(1) ) inbox (clk);
Code Snippet

## Slide 17: Optimizing SCE-MI Pipe Usage
Clearing the pipe
Challenge | Solution
Discarding buffer contents on reset No inbuilt functions Increase in step-count | Use the fastest clock available to synchronously fetch data from pipe
always@(posedge fst_clk, posedge rst) begin
if(rst) begin
rst_buff = 1;
// statements
end
else begin
if(rst_buff && !eom)
inbox.receive(1,ve,data,eom);
else
rst_buff = 0;
end
end
Code Snippet : After
always@(posedge clk, posedge rst) begin
if(rst) begin
// Statements
for(int i=0, i<20), i++)
inbox.receive(1,ve,data,eom);
end
else begin
// statements
end
end
Code Snippet : Before
s
s

## Slide 18: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 19: SCE-MI Direct Memory Interface
Software side interface to perform backdoor read/write operations on hardware side memories
Types of interfaces
  Block interface
  Word interface
Performance Improvement:
  HW-SW synchronizations reduced by ~50%
  TBA run time decreased by >25%

## Slide 20: SCE-MI Direct Memory Interface
Emulator
Simulator
Proxy
Agent
BFM
C Membrane
Memory
DUT
Memory
Backdoor Access
Backdoor Access

## Slide 21: SCE-MI Direct Memory Interface
Proxy side
BFM side
C membrane
Invoke a memory read from BFM
C - Backdoor memory access through predefined SCE-MI API
C-membrane writes the memory contents in to the proxy

## Slide 22: SCE-MI Function Based Interface
Adopts SystemVerilog Direct Programming Interface (DPI) concept.
End user is required to implement all the functions
  No built in functions
Used to configure BFM registers

## Slide 23: SCE-MI Function Based Interface
Proxy
Agent
BFM
C Membrane
Interface
Write Pointer
Read Pointer
Circular FIFO
DUT
Emulator
Simulator

## Slide 24: SCE-MI Function Based Interface
C-function imported and used in proxy
Verilog -function exported and used in the C - interface
BFM register write from C interface
Invoke register write from proxy through C
C membrane
Proxy side
BFM side

## Slide 25: Trimming Development Time
Factors
  Increase in effort and time to implement complex functionality in a synthesizable format.
  Increase in area occupied by the BFM on the emulator.
Implement complex functionality that is utilized occasionally as a method in the C membrane and import/invoke from the BFM.

## Slide 26: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 27: Optimized Architecture
SCEMI Function Based Interface
To configure BFM registers
To update proxy about events in BFM
SCEMI Direct Memory Interface
To write/read data from BFM memory
Pipes are removed

## Slide 28: Agenda
Acceleration Concept
Introduction to SCE-MI and SCE-MI Pipes
Testbench Architecture and Existing Challenges
Optimizing SCE-MI pipe usage
SCE-MI Direct Memory and Function Based Interface
Optimized Architecture
Results and Conclusion

## Slide 29: Results
TBA Performance improvement
Simulation v/s TBA run-time comparison for usecase
Implementation | TBA properties |  |  | 
 | Gate count | Bevals | HW-SW Sync | TBA Time
Pipe only | ~2 M | 18,299,173 | 4,728,998 | ~60 min
Pipes only (Optimized) | ~2 M | 2,859,320 | 1,284,765 | ~35 min
DMI + Function based Interface | ~1.5 M | 218 | 9,871 | ~4 min
Simulation Time | TBA Time
~360min | ~8min

## Slide 30: Conclusion
SCE-MI has multiple interfaces for different use cases
  SCE-MI DMI used for backdoor read/write operation
  SCE-MI Function Based Interface used to write into registers
  SCE-MI Pipes are intended for streaming, variable length messaging, etc.
HW-SW sync and Bevals could greatly deteriorate the performance of emulator.

## Slide 31: Conclusion
Efficient usage of SCE-MI helps in leveraging maximum performance from emulator resulting in handsome SPEED-UP.
HW-SW syncs generated using vendor proprietary implementation
  Number of syncs are kept to minimum.

## Slide 32: Future Work
Porting to SOC environment and analyze the performance
Explore UVM registers support decribed in SCEMI v2.3

## Slide 33: Acknowledgements
David Brownell, ADI
Anilkumar T. S, Cadence
Dr. Hans van der Schoot, Mentor Graphics

## Slide 34
Questions